## Slide 1: PHạM ANH tuấn
THESIS INTERNSHIP 2021-2022
IS THERE A WINDOW OF OPPORTUNITY IN THE WEATHER? WIND SPEED & WAVE HEIGHT FORECASTS FOR OPERATION AND MAINTENANCE OF GEMINI WIND FARM – THE CASE OF JACK-UP VESSEL
Prof. IR. Rommert Dekker
Assoc. Prof. NM Almeida Camacho

## Slide 2: Table of content
1
Introduction
2
Methodology
3
Data analysis
Data imputation results
4
5
Prediction results & analysis
Conclusion
Q&A

## Slide 3
INTRODUCTION
Problem statement
Research questions
Contribution of the thesis
Methodology and data sources

## Slide 4: Thesis TOPIC
MOTIVATION
70%
1/2
The Netherlands Target 2030
Wind farms is being installed further and further offshore in deeper water in Europe (2019)
30%
O&M cost increases as the wind farm is further offshore
3 main activities of the offshore wind farm Operation & Maintenance
PROBLEM
How can Gemini wind farm apply the weather window of wave height and wind speed forecasting in planning the jack-up vessel in an efficient way while ensuring some safety standards?
Notes: 3 main activities of the offshore wind farm Operation & Maintenance
Transportation of maintenance personnel
Shipment of large equipment and component
Lifting activities and safety standards

## Slide 5
RESEARCH QUESTIONS
RQ1
How can the offshore wind farm operator forecast the wind speed over a short-term and long-term period?
RQ2
How can the offshore wind farm operator forecast the wave height over a short-term period?
RQ3
How should the wind farm operator charter the jack-up vessel, in which season of the year, on which day, and for how long given certain maintenance needs?
RQ4
RQ5
How can the wind farm operator determine the trade-off between the revenue gained by 1 day/1 week/1 month delay in maintenance for more energy generation thanks to better weather?
How can the wind farm operator organize the jack-up vessel to conduct maintenance on the wind farm by establishing the trade-off between revenue of the wind farm gained in the delay and the demurrage rate of the jack-up vessel?
RQ3
RQ4
RQ5

## Slide 6
THESIS CONTRIBUTION
Supplements (Schouten, 2019) research by predicting the difference in energy output and downtime cost for certain delay
Provides Synthetic Climate Data Prediction of both the wind speed and the wave height for the accessibility and operative analysis
Provides long-term planning for jack-up vessel
Provides short-term accessibility assessment for jack-up vessel
Applies most updated data
EXCEPT FOR THE FAILURE ANALYSIS, THE THESIS COVERS ALMOST ALL THE TOPICS OF OFFSHORE WIND FARM OPERATION & MAINTENANCE RESEARCH

## Slide 7
DATA SOURCES
CMEMS
Van Oord Aeolus sea keeping specification (Crol, 2015)
Jack-up vessel charter rate (Dalgic, Lazakis, Turan, et al., 2015)
2011 - 2020
2018 - 2021
2017 - 2020
2015
2015
Hourly level
Hourly level
Every 15 minutes
m and m/s
Pound Sterling
2002
METHODOLOGY
QUANTITATIVE RESEARCH
Notes: Research methodology
What data to collect (and what data to ignore)
Who to collect it from (in research, this is called “sampling design”)
How to collect it (this is called “data collection methods”)
How to analyse it (this is called “data analysis methods”)

## Slide 8: Data specification
Weather and power output time series data is non-stationary, not normally distributed, and multi-seasonality with missing values
Chart: Hourly mean wind speed 2011-2012
Frequency of hourly mean wind speed
Wind speed (m/s)
Frequency
Data is skewed to the right
No constant mean
No constant variance
Hourly data with V-shape pattern every year -> at least hourly & yearly seasonality
Hourly mean wind speed time series 2016 -2019
m/s
Year
Variable name | Missing values | The largest number of consecutive missing values
Mean_wind_speed | 3030 | 2424
Temperature | 983 | 312
100 consecutive days 1 season lost
Average energy output every 15 minutes mean wind speed in hourly level and daily level
Notes: Stationarity
To obtain parsimony in a time series model you often assume some form of distributional invariance over time, or stationarity. For an observed time series: Fluctuations appear random. However, the same type of random behavior often holds from one time period to the next. For example, returns on stocks or changes in interest rates each have very different behavior from the previous year. But their mean, standard deviation, and other statistical properties are often similar from one year to the next.
3. Weak stationarity - I
A process is weakly stationary if its mean, variance, and covariance are unchanged by time shifts. That is, there is a common constant mean mu and a variance sigma-squared for all times t.
4. Weak stationarity - II
And, the covariance between Y at time T and at time S only depends on how close T and S are, not the time indices T and S themselves. For example, if Y is a stationary process, then the covariance between Y at times 2 and 5 is the same as that between times 7 and 10, since they are both three time units apart.
5. Stationarity: why?
Why focus on stationary models? A stationary process can be modeled with many fewer parameters. You do not need a different mean for each Y_t; rather they all have a common mean mu. You can estimate mu accurately by y-bar, the sample mean.
6. Stationarity: when?
When a time series is observed, a natural question is: Is it stationary? Specifically, is a stationary process model appropriate for this time series data? Many financial time series do not exhibit stationarity. However: The changes in the series are often approximately stationary. Perhaps after applying a log() transformation. A stationary series should show random oscillation around some fixed level, a phenomenon called mean-reversion.
1. Autocorrelation
Autocorrelation is a very powerful tool for time series analysis. It helps us study how each time series observation is related to its recent past. Processes with greater autocorrelation are more predictable than those with none.
4. Autocorrelations at lag 1 and 2 - I
The autocorrelation function or ACF is simply the autocorrelation defined as a function of the time lag, 1, 2, etc

## Slide 9
METHODOLOGY
Data pre-processing method
Data decomposition method
Time series prediction methods
Model validation methods

## Slide 10
Data Pre-processing
Data Decomposition
Large number of missing observations
Random Forest Imputation
Data is not normally distributed
Box-Cox transformation
Different granularity in wind energy
Mathematical transformation
Multi-seasonality
Seasonal & Trend decomposition using Loess (STL)
Seasonal components
Trend
Remainder
Prediction methods
Validation methods
No constant mean
No constant variance
Long-term (daily data)
Short–term (hourly data)
Dynamic Harmonic Regression using Fourier Terms (F-ARMA)
Non-linear Autoregressive Neural Network (NARX – NAR)
Root Mean Squared Error (RMSE)
Mean Absolute Percentage Error (MAPE)
Winkler Score
Continuous Rank Probability Score (CRPS)
Time series Cross Validation (tsCV)
Corrected Akaike’s Information Criterion (AICc)
Ljung-Box test
Point forecast accuracy
Forecast distribution accuracy
Model selection criteria
Short-term prediction
Long-term prediction

## Slide 11
Offshore wind energy output transformation 2017 - 2020
Proportion of offshore energy generated by Gemini wind farm based on nominal energy output
Wind power generated per wind turbine in Gemini wind farm
Actual offshore wind energy generated in the Netherlands every hour on average
Actual offshore wind energy generated in The Netherlands every 15 minutes
with
= }
with
=
Wind farm | Capacity wind farm (MW) | Proportion (%) | In use since
Borssele V (Innovation site) | 19 | 0.77 | 2021
Borssele I & II | 752 | 30.57 | 2020
Borssele III & IV | 731.5 | 29.74 | 2020
Gemini | 600 | 24.39 | 2016
Luchterduinen | 129 | 5.24 | 2015
Prinses Amalia | 120 | 4.88 | 2008
Egmond aan Zee (OWEZ) | 108 | 4.41 | 2007
Total | 2459.5 |  | 
Month | Gemini capacity (MW) | Borssele I & II capacity (MW) | Borssele III & IV capacity (MW) | Gemini energy output proportion in The Netherlands (%)
January - March | 600 | 0 | 0 | 62.69
April | 600 | 12 x 8 | 0 | 57
May | 600 | 24 x 8 | 0 | 52
June | 600 | 36 x 8 | 0 | 48
July | 600 | 48 x 8 | 0 | 44
August | 600 | 60 x 8 | 19 x 9.5 | 37
September | 600 | 72 x 8 | 38 x 9.5 | 31
October | 600 | 94 x 8 | 57 x 9.5 | 26
Nov to Dec | 600 | 94 x 8 | 77 x 9.5 | 24.60
Disadvantage
Does not consider the energy lost due to daily maintenance
The energy generated is not consistent with the same given wind speed
Might affect the accuracy of the prediction model

## Slide 12
Random Forest Imputation
Fill in the missing values with the median
Build a random forest consisting different trees
Run all the data through all the trees to find the similar sample of the sample with missing data (end up at same leaf node)
Keep track of the similarity decided by each tree with “proximity matrix”
Then divide each proximity value with the total number of trees
The missing value is considered as the sum of each sample value multiplied by its weighted average based on the proximity matrix
Repeat the process all over again until the missing value converge
Observation | Hour | Day | Month | Year | Temp | Wind speed
1 | 0 | 1 | 5 | 2014 | 12 | 4
2 | 1 | 1 | 5 | 2014 | 14 | 5
3 | 2 | 1 | 5 | 2014 | 13 | 6
4 | 3 | 1 | 5 | 2014 | 11 | ??
Original data set
Observation | Hour | Day | Month | Year | Temp | Wind speed
1 | 0 | 1 | 5 | 2014 | 12 | 4
2 | 1 | 1 | 5 | 2014 | 14 | 5
3 | 2 | 1 | 5 | 2014 | 13 | 6
4 | 3 | 1 | 5 | 2014 | 11 | 5
 | 1 | 2 | 3 | 4
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 1
4 |  |  | 1 | 
 | 1 | 2 | 3 | 4
1 |  |  |  | 
2 |  |  | 1 | 1
3 |  | 1 |  | 2
4 |  | 1 | 2 | 
 | 1 | 2 | 3 | 4
1 |  |  |  | 
2 |  |  | 0.5 | 0.5
3 |  | 0.5 |  | 1
4 |  | 0.5 | 1 | 
Weighted average = 4x0 + 5x + 6x = 5.67
Fill in the missing values with the median
Original data set

## Slide 13
Seasonal & Trend decomposition using Loess (STL)
Dynamic Harmonic Regression using Fourier Terms (F-ARMA)
Time series
Advantage
Disadvantage
Automatically capture and decompose the time series without prior assumptions of trend and seasonality
Supports the Fourier prediction in defining the multi-seasonality of the time series and selecting the number of Fourier terms
Robust to multi-seasonal, non-stationary, and non-linear time series
the components might not have the same unit of measurement as the original time series
Periodic seasonality can be captured by different pairs of Fourier terms
: seasonal period length
number of pairs of Fourier terms
regression coefficients
can be modeled as non-seasonal ARIMA process
Assume seasonal pattern is unchanged
Advantage
Can be constructed with any seasonal period length, especially for large period time series as daily, sub-daily time series
Can capture the multi-seasonality nature of our data set
K
Disadvantage
Unchanged seasonal pattern might be unrealistic
Notes: 1. STL
After several reviews of wind speed and wave height prediction methods, we saw that the weather indices time series were reported with multiple seasonality, non – stationary, and non-linear trends in data Heaton et al., 2019 Huang and Dong, 2021 for example. In addition, specifying the type of seasonality, trend, and their impact on the existing time series is crucial to capture the variance of the data in the statistical modeling beside visual diagnosis. Therefore, in current research, for more accurate quantitative analysis to discover the trend and seasonality of the chosen weather time series, “Seasonal and Trend decomposition using Loess,”(Cleveland et al., 1990) or STL for short was applied to the time series before constructing prediction model. Because STL is a filtering process that can evaluate and decompose the time series into trend, the multi-seasonality, and the remaining components robustly with different granularities and missing values, it was applied to wind speed time series as in Laib et al., 2018, Guignard et al., 2019. For significant wave height time series, Yang et al., (2021) also applied STL decomposition to the wave height times series before using a convolutional neural network for forecasting. This decomposition method was also applied to significant wave height data in Ramachandra, (2019) and Rodolfo Piscopia, (2015).
STL decomposition is also useful in measuring the strength of trend and seasonality of the data
3. Dynamic harmonic regression
A series of sine and cosine terms of the right frequencies can approximate any periodic function. We can use them for seasonal patterns when forecasting. Fourier terms come in pairs consisting of a sine and a cosine. The frequency of these terms are called the "harmonic frequencies", and they increase with k. These Fourier terms are predictors in our dynamic regression model. The more terms we include in the model, the more complicated our seasonal pattern will be. We choose uppercase K to control how many terms get included. The alpha and gamma values are coefficients in our regression model. Because the seasonality is being modelled by the Fourier terms, we normally use a non-seasonal ARIMA model for the error. One important difference between handling seasonality this way, and using a seasonal ARIMA model, is that Fourier terms assume the seasonal pattern does not change over time, whereas a seasonal ARIMA model allows the seasonal pattern to evolve over time.
This Fourier – ARIMA model assumes that the seasonal pattern does not change over time which is suitable for the average daily mean wind speed since its yearly seasonal components have the same pattern over time as in Figure 22. It is also the strongest seasonal component in the time series. The only concern is the weekly seasonal components fluctuate more wildly as in Figure 22, which may affect the accuracy of the model.
One more advantage of Fourier – ARIMA over the Seasonal ARIMA and Exponential Smoothing methods with Trends and Seasonality (ETS) is that Fourier – ARIMA can be constructed with any seasonal period length, especially for large period time series as daily time series (Rob J Hyndman, 2021).
Thirdly, since the average daily mean wind speed time series has both weekly and yearly seasonal components, Fourier – ARIMA can develop different Fourier terms for different seasonal periods separately. This enables the model to handle the multi-seasonality nature of our data set. In addition, the smaller the is, the smoother the seasonal pattern. In addition, the value of is not larger than half of the seasonal period length . Therefore, we can choose based on the given selection criteria which will be discussed in section 2.2.,
Finally, although Seasonal ARIMA allows the seasonality of the time series to change over the period under the study, in this case, the annual seasonal pattern is substantially constant. In addition, because the annual and weekly seasonal patterns are not smooth, it does not make sense to make the seasonal differencing of one year, or in another word, compare the current value with the observation one year ago.
1. STL
After several reviews of wind speed and wave height prediction methods, we saw that the weather indices time series were reported with multiple seasonality, non – stationary, and non-linear trends in data Heaton et al., 2019 Huang and Dong, 2021 for example. In addition, specifying the type of seasonality, trend, and their impact on the existing time series is crucial to capture the variance of the data in the statistical modeling beside visual diagnosis. Therefore, in current research, for more accurate quantitative analysis to discover the trend and seasonality of the chosen weather time series, “Seasonal and Trend decomposition using Loess,”(Cleveland et al., 1990) or STL for short was applied to the time series before constructing prediction model. Because STL is a filtering process that can evaluate and decompose the time series into trend, the multi-seasonality, and the remaining components robustly with different granularities and missing values, it was applied to wind speed time series as in Laib et al., 2018, Guignard et al., 2019. For significant wave height time series, Yang et al., (2021) also applied STL decomposition to the wave height times series before using a convolutional neural network for forecasting. This decomposition method was also applied to significant wave height data in Ramachandra, (2019) and Rodolfo Piscopia, (2015).
STL decomposition is also useful in measuring the strength of trend and seasonality of the data
3. Dynamic harmonic regression
A series of sine and cosine terms of the right frequencies can approximate any periodic function. We can use them for seasonal patterns when forecasting. Fourier terms come in pairs consisting of a sine and a cosine. The frequency of these terms are called the "harmonic frequencies", and they increase with k. These Fourier terms are predictors in our dynamic regression model. The more terms we include in the model, the more complicated our seasonal pattern will be. We choose uppercase K to control how many terms get included. The alpha and gamma values are coefficients in our regression model. Because the seasonality is being modelled by the Fourier terms, we normally use a non-seasonal ARIMA model for the error. One important difference between handling seasonality this way, and using a seasonal ARIMA model, is that Fourier terms assume the seasonal pattern does not change over time, whereas a seasonal ARIMA model allows the seasonal pattern to evolve over time.
This Fourier – ARIMA model assumes that the seasonal pattern does not change over time which is suitable for the average daily mean wind speed since its yearly seasonal components have the same pattern over time as in Figure 22. It is also the strongest seasonal component in the time series. The only concern is the weekly seasonal components fluctuate more wildly as in Figure 22, which may affect the accuracy of the model.
One more advantage of Fourier – ARIMA over the Seasonal ARIMA and Exponential Smoothing methods with Trends and Seasonality (ETS) is that Fourier – ARIMA can be constructed with any seasonal period length, especially for large period time series as daily time series (Rob J Hyndman, 2021).
Thirdly, since the average daily mean wind speed time series has both weekly and yearly seasonal components, Fourier – ARIMA can develop different Fourier terms for different seasonal periods separately. This enables the model to handle the multi-seasonality nature of our data set. In addition, the smaller the 𝐾 is, the smoother the seasonal pattern. In addition, the value of 𝐾 is not larger than half of the seasonal period length 𝑚. Therefore, we can choose 𝐾 based on the given selection criteria which will be discussed in section 2.2.,
Finally, although Seasonal ARIMA allows the seasonality of the time series to change over the period under the study, in this case, the annual seasonal pattern is substantially constant. In addition, because the annual and weekly seasonal patterns are not smooth, it does not make sense to make the seasonal differencing of one year, or in another word, compare the current value with the observation one year ago.

## Slide 14
Non-linear Autoregressive Neural Network (NARX – NAR)
Can handle non-linear relationship
Advantage
Adaptive learning
Robust to missing values
Disadvantage
Lack of interpretability
Short forecasting horizon ( < 24 time steps)
Prediction results are not stable
: number of lag inputs
: number of seasonal lag inputs
: number of neurons in hidden layers
: seasonal period
Notes: 1. NAR + NARX The Non-linear Auto-regressive Neural Network with Exogenous inputs is the neural network structure that resembles the brain structure and nodes are organized in different layers. The top layer is the output of the prediction, and the bottom layer is the set of input values which are the time lag of the response and independent variables. In between these two layers are intermediate layers containing “hidden nodes” or “hidden neurons” (Rob J Hyndman, 2021). In R, we used the fable package (Mitchell O'Hara-Wild, 2021) which applies the multilayer feed-forward network with 1 layer of hidden nodes. In this neural network, lagged values of the response and exogenous variables are used as predictors in the input layer. In addition, the previous layer of nodes creates input for the next layer of nodes.
In this neural network structure, the “weights” are the coefficients attached to these predictors. The weights are selected in the neural network framework using a “learning algorithm” that minimizes a “cost function” such as the Mean Squared Error (MSE) or Mean Absolute Percentage Error(MAPE). In the hidden layer, we apply a weighted linear combination to the inputs before transferring them to each hidden node. For example, the weighted linear combination is (Rob J Hyndman, 2021):
(3)
We then adjust the results by non-linear function like the sigmoid function below before being the output or being transferred to the next layer (Rob J Hyndman, 2021):
In this thesis, we denote the Non-linear Auto-Regressive Neural network with Exogenous inputs as and Non-linear Auto-Regressive Neural network as to indicate lagged inputs, neurons in the hidden layer, is the number of seasonal lagged inputs, is the seasonal period. The fable package automatically chooses the value of with the default value of is 1, is selected from the optimal linear model fitted to the seasonally adjusted data, and (rounded to the nearest integer). For multi-step-ahead forecasting, we use the one-step ahead and historical data as inputs and continue this process until we complete the forecast horizon (Mitchell O'Hara-Wild, 2021).
2. Winkler score
To measure the accuracy of the prediction interval for the wind speed, we apply the Winkler score to check how far one actual observation lies within or outside of the prediction interval (Winkler, 1972). If the prediction interval at time is defined by , the Winkler score is the interval length with the penalty for the observation which is outside the interval:
(9)
We can see that if the observation lies in between the prediction interval, the Winkler score is the interval length, and it is small. Whereas, if the observation falls outside the interval, the penalty will be proportional to the distance between the observation and the interval, which makes the Winkler score larger.
3. CRPS
To establish a weather window of the average daily wind speed, we need to evaluate the accuracy of the whole forecasting distribution. Therefore, we can apply the Continuous Ranked Probability Score (CRPS) proposed by Gneiting and Katzfuss, 2014.
First, we calculate the quantile forecast of probability at time . If we denote as an observation at time , then with the 20th percentile, we have and is expected to be less than with the probability of 20%. Then the Quantile Score is defined as:
(10)
The Quantile score can be considered as an absolute error if = 0.5. If > 0.5 then will place a heavier penalty to than when and vice versa.
The CRPS is an average of over all values of therefore, it takes the average for each of the predictive densities and the corresponding observation over the period under the study. The CRPS and Mean Absolute Error (MAE) (for deterministic forecasting) are directedly comparable since CRPS is the generalization of MAE with a given lead time and nominal/normalized scale. Given the same lead time, nominal scale, and data set, if a probabilistic forecast has a CRPS value of 7%, it is better than the deterministic forecast with the MAE value of 8%. The lower the CRPS, the better the prediction distribution
1. NAR + NARX The Non-linear Auto-regressive Neural Network with Exogenous inputs is the neural network structure that resembles the brain structure and nodes are organized in different layers. The top layer is the output of the prediction, and the bottom layer is the set of input values which are the time lag of the response and independent variables. In between these two layers are intermediate layers containing “hidden nodes” or “hidden neurons” (Rob J Hyndman, 2021). In R, we used the fable package (Mitchell O'Hara-Wild, 2021) which applies the multilayer feed-forward network with 1 layer of hidden nodes. In this neural network, lagged values of the response and exogenous variables are used as predictors in the input layer. In addition, the previous layer of nodes creates input for the next layer of nodes.
In this neural network structure, the “weights” are the coefficients attached to these predictors. The weights are selected in the neural network framework using a “learning algorithm” that minimizes a “cost function” such as the Mean Squared Error (MSE) or Mean Absolute Percentage Error(MAPE). In the hidden layer, we apply a weighted linear combination to the inputs before transferring them to each hidden node. For example, the weighted linear combination is (Rob J Hyndman, 2021):
𝑧_𝑗=𝑏_𝑗+∑1_(𝑖=1)^𝑛▒〖𝑤_(𝑖,𝑗) 𝑥_𝑖 〗 (3)
We then adjust the results by non-linear function like the sigmoid function below before being the output or being transferred to the next layer (Rob J Hyndman, 2021):
𝑠(𝑧) = 1/(1+𝑒^(−𝑧) )
In this thesis, we denote the Non-linear Auto-Regressive Neural network with Exogenous inputs as〖 𝑁𝐴𝑅𝑋(𝑝,𝑃,𝑘)〗_𝑚 and Non-linear Auto-Regressive Neural network as 〖𝑁𝐴𝑅(𝑝,𝑃,𝑘)〗_𝑚 to indicate 𝑝 lagged inputs, 𝑘 neurons in the hidden layer, 𝑃 is the number of seasonal lagged inputs, 𝑚 is the seasonal period. The fable package automatically chooses the value of 𝑝,𝑃,𝑘 with the default value of 𝑃 is 1, 𝑝 is selected from the optimal linear model fitted to the seasonally adjusted data, and 𝑘 = (𝑝+𝑃+1)/2 (rounded to the nearest integer). For multi-step-ahead forecasting, we use the one-step ahead and historical data as inputs and continue this process until we complete the forecast horizon (Mitchell O'Hara-Wild, 2021).
2. Winkler score
To measure the accuracy of the prediction interval for the wind speed, we apply the Winkler score to check how far one actual observation lies within or outside of the prediction interval (Winkler, 1972). If the 100(1−𝛼)% prediction interval at time 𝑡 is defined by [𝑙_(𝛼,𝑡);ℎ_(𝛼,𝑡) ], the Winkler score is the interval length with the penalty for the observation which is outside the interval:
{█(𝑊_(𝛼,𝑡)=(ℎ_(𝛼,𝑡)−𝑙_(𝛼,𝑡) )+2/𝛼 (𝑙_(𝛼,𝑡)− 𝑦_𝑡 ) 𝑖𝑓 𝑦_𝑡< 𝑙_(𝛼,𝑡) @𝑊_(𝛼,𝑡)= (ℎ_(𝛼,𝑡)−𝑙_(𝛼,𝑡) ) 𝑖𝑓 𝑙_(𝛼,𝑡) ≤ 𝑦_𝑡 ≤ℎ_(𝛼,𝑡)@𝑊_(𝛼,𝑡)= (ℎ_(𝛼,𝑡)−𝑙_(𝛼,𝑡) )+ 2/𝛼 ( 𝑦_𝑡 〖−ℎ〗_(𝛼,𝑡) ) 𝑖𝑓 𝑦_𝑡> 𝑙_(𝛼,𝑡) )┤ (9)
We can see that if the observation lies in between the prediction interval, the Winkler score is the interval length, and it is small. Whereas, if the observation falls outside the interval, the penalty will be proportional to the distance between the observation and the interval, which makes the Winkler score larger.
3. CRPS
To establish a weather window of the average daily wind speed, we need to evaluate the accuracy of the whole forecasting distribution. Therefore, we can apply the Continuous Ranked Probability Score (CRPS) proposed by Gneiting and Katzfuss, 2014.
First, we calculate the quantile forecast 𝑓_(𝑝,𝑡) of probability 𝑝 at time 𝑡. If we denote 𝑦_𝑡 as an observation at time 𝑡, then with the 20th percentile, we have 𝑓_(0.2,𝑡) and 𝑦_𝑡 is expected to be less than 𝑓_(0.2,𝑡) with the probability of 20%. Then the Quantile Score 𝑄_(𝑝,𝑡) is defined as:
𝑄_(𝑝,𝑡)= {█(2×(1−𝑝)(𝑓_(𝑝,𝑡)− 𝑦_𝑡 ) 𝑖𝑓 𝑦_𝑡< 𝑓_(𝑝,𝑡)@2×𝑝(𝑦_𝑡−𝑓_(𝑝,𝑡) ) 𝑖𝑓 𝑦_𝑡 ≥ 𝑓_(𝑝,𝑡) )┤ (10)
The Quantile score 𝑄_(𝑝,𝑡) can be considered as an absolute error if 𝑝 = 0.5. If 𝑝 > 0.5 then 𝑄_(𝑝,𝑡) will place a heavier penalty to 𝑦_𝑡>𝑓_(𝑝,𝑡) than when 𝑦_𝑡<𝑓_(𝑝,𝑡) and vice versa.
The CRPS is an average of 𝑄_(𝑝,𝑡) over all values of 𝑝 therefore, it takes the average for each of the predictive densities and the corresponding observation over the period under the study. The CRPS and Mean Absolute Error (MAE) (for deterministic forecasting) are directedly comparable since CRPS is the generalization of MAE with a given lead time and nominal/normalized scale. Given the same lead time, nominal scale, and data set, if a probabilistic forecast has a CRPS value of 7%, it is better than the deterministic forecast with the MAE value of 8%. The lower the CRPS, the better the prediction distribution

## Slide 15
Non-linear Autoregressive Neural Network (NARX – NAR)
Validation methods
computed in parallel and online to accelerate the speed of the model
Advantage
Adaptive learning via the training process and construct their structure to represent the data
Robust to missing values or damaged structure in the data
Disadvantage
Lack of interpretability
Short forecasting horizon ( < 24 time steps)
Prediction results are not stable
: number of lag inputs
: number of seasonal lag inputs
: number of neurons in hidden layers
: seasonal period
Winkler score
Continuous Rank Probability Score (CRPS)
: the prediction interval at time
Winkler score is the interval length with the penalty for the observation which is outside the interval. The smaller Winkler score, the narrower the prediction interval is and the more credible it is
Quantile Score
: quantile forecast of probability at time
: quantile score. It can be interpreted as the absolute error. The lower the quantile score is, the better the estimation of the quantile is
: The average of for all value of over the period under study. The lower the CRPS is, the better the forecast distribution
Notes: 1. NAR + NARX The Non-linear Auto-regressive Neural Network with Exogenous inputs is the neural network structure that resembles the brain structure and nodes are organized in different layers. The top layer is the output of the prediction, and the bottom layer is the set of input values which are the time lag of the response and independent variables. In between these two layers are intermediate layers containing “hidden nodes” or “hidden neurons” (Rob J Hyndman, 2021). In R, we used the fable package (Mitchell O'Hara-Wild, 2021) which applies the multilayer feed-forward network with 1 layer of hidden nodes. In this neural network, lagged values of the response and exogenous variables are used as predictors in the input layer. In addition, the previous layer of nodes creates input for the next layer of nodes.
In this neural network structure, the “weights” are the coefficients attached to these predictors. The weights are selected in the neural network framework using a “learning algorithm” that minimizes a “cost function” such as the Mean Squared Error (MSE) or Mean Absolute Percentage Error(MAPE). In the hidden layer, we apply a weighted linear combination to the inputs before transferring them to each hidden node. For example, the weighted linear combination is (Rob J Hyndman, 2021):
(3)
We then adjust the results by non-linear function like the sigmoid function below before being the output or being transferred to the next layer (Rob J Hyndman, 2021):
In this thesis, we denote the Non-linear Auto-Regressive Neural network with Exogenous inputs as and Non-linear Auto-Regressive Neural network as to indicate lagged inputs, neurons in the hidden layer, is the number of seasonal lagged inputs, is the seasonal period. The fable package automatically chooses the value of with the default value of is 1, is selected from the optimal linear model fitted to the seasonally adjusted data, and (rounded to the nearest integer). For multi-step-ahead forecasting, we use the one-step ahead and historical data as inputs and continue this process until we complete the forecast horizon (Mitchell O'Hara-Wild, 2021).
2. Winkler score
To measure the accuracy of the prediction interval for the wind speed, we apply the Winkler score to check how far one actual observation lies within or outside of the prediction interval (Winkler, 1972). If the prediction interval at time is defined by , the Winkler score is the interval length with the penalty for the observation which is outside the interval:
(9)
We can see that if the observation lies in between the prediction interval, the Winkler score is the interval length, and it is small. Whereas, if the observation falls outside the interval, the penalty will be proportional to the distance between the observation and the interval, which makes the Winkler score larger.
3. CRPS
To establish a weather window of the average daily wind speed, we need to evaluate the accuracy of the whole forecasting distribution. Therefore, we can apply the Continuous Ranked Probability Score (CRPS) proposed by Gneiting and Katzfuss, 2014.
First, we calculate the quantile forecast of probability at time . If we denote as an observation at time , then with the 20th percentile, we have and is expected to be less than with the probability of 20%. Then the Quantile Score is defined as:
(10)
The Quantile score can be considered as an absolute error if = 0.5. If > 0.5 then will place a heavier penalty to than when and vice versa.
The CRPS is an average of over all values of therefore, it takes the average for each of the predictive densities and the corresponding observation over the period under the study. The CRPS and Mean Absolute Error (MAE) (for deterministic forecasting) are directedly comparable since CRPS is the generalization of MAE with a given lead time and nominal/normalized scale. Given the same lead time, nominal scale, and data set, if a probabilistic forecast has a CRPS value of 7%, it is better than the deterministic forecast with the MAE value of 8%. The lower the CRPS, the better the prediction distribution
1. NAR + NARX The Non-linear Auto-regressive Neural Network with Exogenous inputs is the neural network structure that resembles the brain structure and nodes are organized in different layers. The top layer is the output of the prediction, and the bottom layer is the set of input values which are the time lag of the response and independent variables. In between these two layers are intermediate layers containing “hidden nodes” or “hidden neurons” (Rob J Hyndman, 2021). In R, we used the fable package (Mitchell O'Hara-Wild, 2021) which applies the multilayer feed-forward network with 1 layer of hidden nodes. In this neural network, lagged values of the response and exogenous variables are used as predictors in the input layer. In addition, the previous layer of nodes creates input for the next layer of nodes.
In this neural network structure, the “weights” are the coefficients attached to these predictors. The weights are selected in the neural network framework using a “learning algorithm” that minimizes a “cost function” such as the Mean Squared Error (MSE) or Mean Absolute Percentage Error(MAPE). In the hidden layer, we apply a weighted linear combination to the inputs before transferring them to each hidden node. For example, the weighted linear combination is (Rob J Hyndman, 2021):
𝑧_𝑗=𝑏_𝑗+∑1_(𝑖=1)^𝑛▒〖𝑤_(𝑖,𝑗) 𝑥_𝑖 〗 (3)
We then adjust the results by non-linear function like the sigmoid function below before being the output or being transferred to the next layer (Rob J Hyndman, 2021):
𝑠(𝑧) = 1/(1+𝑒^(−𝑧) )
In this thesis, we denote the Non-linear Auto-Regressive Neural network with Exogenous inputs as〖 𝑁𝐴𝑅𝑋(𝑝,𝑃,𝑘)〗_𝑚 and Non-linear Auto-Regressive Neural network as 〖𝑁𝐴𝑅(𝑝,𝑃,𝑘)〗_𝑚 to indicate 𝑝 lagged inputs, 𝑘 neurons in the hidden layer, 𝑃 is the number of seasonal lagged inputs, 𝑚 is the seasonal period. The fable package automatically chooses the value of 𝑝,𝑃,𝑘 with the default value of 𝑃 is 1, 𝑝 is selected from the optimal linear model fitted to the seasonally adjusted data, and 𝑘 = (𝑝+𝑃+1)/2 (rounded to the nearest integer). For multi-step-ahead forecasting, we use the one-step ahead and historical data as inputs and continue this process until we complete the forecast horizon (Mitchell O'Hara-Wild, 2021).
2. Winkler score
To measure the accuracy of the prediction interval for the wind speed, we apply the Winkler score to check how far one actual observation lies within or outside of the prediction interval (Winkler, 1972). If the 100(1−𝛼)% prediction interval at time 𝑡 is defined by [𝑙_(𝛼,𝑡);ℎ_(𝛼,𝑡) ], the Winkler score is the interval length with the penalty for the observation which is outside the interval:
{█(𝑊_(𝛼,𝑡)=(ℎ_(𝛼,𝑡)−𝑙_(𝛼,𝑡) )+2/𝛼 (𝑙_(𝛼,𝑡)− 𝑦_𝑡 ) 𝑖𝑓 𝑦_𝑡< 𝑙_(𝛼,𝑡) @𝑊_(𝛼,𝑡)= (ℎ_(𝛼,𝑡)−𝑙_(𝛼,𝑡) ) 𝑖𝑓 𝑙_(𝛼,𝑡) ≤ 𝑦_𝑡 ≤ℎ_(𝛼,𝑡)@𝑊_(𝛼,𝑡)= (ℎ_(𝛼,𝑡)−𝑙_(𝛼,𝑡) )+ 2/𝛼 ( 𝑦_𝑡 〖−ℎ〗_(𝛼,𝑡) ) 𝑖𝑓 𝑦_𝑡> 𝑙_(𝛼,𝑡) )┤ (9)
We can see that if the observation lies in between the prediction interval, the Winkler score is the interval length, and it is small. Whereas, if the observation falls outside the interval, the penalty will be proportional to the distance between the observation and the interval, which makes the Winkler score larger.
3. CRPS
To establish a weather window of the average daily wind speed, we need to evaluate the accuracy of the whole forecasting distribution. Therefore, we can apply the Continuous Ranked Probability Score (CRPS) proposed by Gneiting and Katzfuss, 2014.
First, we calculate the quantile forecast 𝑓_(𝑝,𝑡) of probability 𝑝 at time 𝑡. If we denote 𝑦_𝑡 as an observation at time 𝑡, then with the 20th percentile, we have 𝑓_(0.2,𝑡) and 𝑦_𝑡 is expected to be less than 𝑓_(0.2,𝑡) with the probability of 20%. Then the Quantile Score 𝑄_(𝑝,𝑡) is defined as:
𝑄_(𝑝,𝑡)= {█(2×(1−𝑝)(𝑓_(𝑝,𝑡)− 𝑦_𝑡 ) 𝑖𝑓 𝑦_𝑡< 𝑓_(𝑝,𝑡)@2×𝑝(𝑦_𝑡−𝑓_(𝑝,𝑡) ) 𝑖𝑓 𝑦_𝑡 ≥ 𝑓_(𝑝,𝑡) )┤ (10)
The Quantile score 𝑄_(𝑝,𝑡) can be considered as an absolute error if 𝑝 = 0.5. If 𝑝 > 0.5 then 𝑄_(𝑝,𝑡) will place a heavier penalty to 𝑦_𝑡>𝑓_(𝑝,𝑡) than when 𝑦_𝑡<𝑓_(𝑝,𝑡) and vice versa.
The CRPS is an average of 𝑄_(𝑝,𝑡) over all values of 𝑝 therefore, it takes the average for each of the predictive densities and the corresponding observation over the period under the study. The CRPS and Mean Absolute Error (MAE) (for deterministic forecasting) are directedly comparable since CRPS is the generalization of MAE with a given lead time and nominal/normalized scale. Given the same lead time, nominal scale, and data set, if a probabilistic forecast has a CRPS value of 7%, it is better than the deterministic forecast with the MAE value of 8%. The lower the CRPS, the better the prediction distribution

## Slide 16
IMPUTATION & ANALYSIS RESULTS
Hourly mean wind speed
Hourly mean wind power
Daily average mean wind speed
Hourly significant wave height

## Slide 17
Hourly mean wind speed imputation results
 |  | ntree = 2 & mtry = | ntree = 10 & mtry = | ntree = 25 & mtry = | ntree = 50 & mtry = 7
OOB error (MSE) | Mean_wind_speed | 0.79 | 0.58 | 0.52 | 0.52
 | Temperature | 1.49 | 1.10 | 0.88 | 0.49
Computation time (minutes) |  | 11.23 | 44 | 154.87 | 352.51
 |  |  |  |  | ntree = 50 & mtry = 7
OOB error (MSE) | Mean_wind_speed | 0.79 | 0.58 | 0.52 | 0.52
 | Temperature | 1.49 | 1.10 | 0.88 | 0.49
Computation time (minutes) |  | 11.23 | 44 | 154.87 | 352.51
Chart: Hourly mean wind speed 2011-2012 after imputation with mtry =7 and ntree = 50
ntree: Number of decision trees in the random forest
mtry: Number of variables used to build the decision tree
Data imputed by random forest imputation with ntree = 50 and mtry = 7 was selected due to its lowest Out-of-bag (OOB) error
Keeps the variance of the weather data instead of a straight line like other linear imputation methods
Smaller variance
The missing values only account for around 3% of the data set.
Missing value imputation does not increase the information of the data set but prevents the loss of information when applying data analysis methods that require complete data.

## Slide 18
2 wind and wave seasons coincide with the seasonal chartering rates
Winter: October to March with higher medians
Parameter | Value
Daily charter rate (Pound) | 172500 Pound/day (April – September)
 | 116250 Pound/day (October – March)
Demurrage (Pound) | +30% daily rate
Jack-up/down period | 3 hours
Hub removal time | 8 hours
Jack-up vessel charter rate is seasonal which is lower in the winter and higher in the summer
Summer: April to September with lower medians

## Slide 19
Deceasing wind speed and wind energy trend stress on better vessel scheduling and weather window prediction
The strongest yearly_seasonal component with V-shape pattern with the lowest wind speed and wind energy in the middle of every year (June, July, September)
Wind speed at 10-meter height 2015 - 2019
Wind energy at Gemini 2017-2020
The middle of the year is the busiest season of jack-up vessel with low availability and high prices
Can we schedule the jack-up vessel in the decreasing wind period to be safer and less costly?

## Slide 20
PREDICTION RESULTS & ANALYSIS
Long-term average daily mean wind speed prediction
Weather window analysis
Short-term hourly mean wind speed & power prediction
Short-term hourly significant wave height prediction

## Slide 21
Wind speed trend
Jan
Feb
Mar
Apr
May
Long-term forecast
Long-term wind speed prediction
Average daily mean wind speed
- Weather window forecast and selection
- Scheduling and sharing the jack-up vessel between wind farms
Short-term prediction with hourly data
- Accessibility & safety of O&M activities on site
- Determine the trade-off between the revenue gained by the delay and demurrage rate
Weather window analysis process for jack-up vessel and gearbox at Gemini offshore wind farm
Short-term forecast

## Slide 22
Dynamic Harmonic Regression was applied to average daily mean wind speed since there are both weekly and yearly seasonal components in the daily time series
Average daily mean wind speed
F-ARMA(3,2)x(1,0,0)
Lowest AICc
F-ARMA(3,2)x(1,0,0)xTemp
 | AICc | RMSE |  | MAPE |  | Winkler Score | CRPS | tsCV RMSE | Ljung-Box test P-value | Conclusion
 |  | Train | Test | Train | Test |  |  |  |  | 
F-ARMA(3,2)x(1,0,0) | 3928.50 | 2.15 | 2.60 | 27.71 | 34.72 | 11.1 | 1.46 | - | 0.61 | Uncorrelated residuals
F-ARMA(3,20)x(1,0,0) | 3972.56 | 2.13 | 2.58 | 27.68 | 35.6 | 10.9 | 1.45 | - | 0.08 | Uncorrelated residuals
F-ARMA(3,2)x(1,0,0)xTemp | 3905.86 | 2.13 | 2.60 | 27.38 | 34.0 | 11.20 | 1.36 | 2.60 | 0.71 | Uncorrelated residuals
Seasonal Naïve model | NA | NA | 3.58 | NA | 51.53 | 142 | 5.08 | 3.55 | 0.00 | Correlated residuals
Ensure the assumptions of residuals

## Slide 23
For the prediction of 2020, the forecast distribution and mean point forecasts of F-ARMA(3,2)x(1,0,0)xTemp can capture the variance of real observations, satisfied the residual assumptions, and model parsimony
Chart: 95% Prediction interval and point forecast of F-ARMA(3,2)x(1,0,0)
Chart: 95% Prediction interval and point forecast of F-ARMA(3,20)x(1,0,0)
Chart: 95% Prediction interval and point forecast of F-ARMA(3,2)x(1,0,0)xTemp

## Slide 24
Dynamic Harmonic Regression with 3 pairs of Fourier terms for weekly seasonality and 2 pairs of Fourier terms for yearly seasonality and Temperature as exogenous input
Where
F-ARMA(3,2)x(1,0,0)xTemp
Fourier terms for yearly seasonality
Fourier terms for weekly seasonality
Notes: With = 0,1,2…, the pairs of Fourier terms represent the weekly and yearly seasonality of the average daily mean wind speed after Box-Cox transformation in the corresponding timestep. In addition, After Box-Cox transformation with = 0,1,2…, if other factors stay the same, Temp(t) increases by 1 unit will make the wind speed ybt increase by 0.036 unit.
Although this type of model has a MAPE of 35.5 which means on average, its error of point forecasting is 35% as large as the real wind speed value, the purpose of long–term wind speed forecasting is to establish the wind speed window which focuses more on the forecasting distribution. Therefore, the smallest CRPS of 1.43 is acceptable.
With 𝑡 = 0,1,2…, the pairs of Fourier terms represent the weekly and yearly seasonality of the average daily mean wind speed after Box-Cox transformation in the corresponding timestep. In addition, After Box-Cox transformation with 𝑡 = 0,1,2…, if other factors stay the same, Temp(t) increases by 1 unit will make the wind speed ybt increase by 0.036 unit.
Although this type of model has a MAPE of 35.5 which means on average, its error of point forecasting is 35% as large as the real wind speed value, the purpose of long–term wind speed forecasting is to establish the wind speed window which focuses more on the forecasting distribution. Therefore, the smallest CRPS of 1.43 is acceptable.

## Slide 25
Chart: Wind speed weather window for Gemini wind farm at 89.5 meter height
Chart: Wind speed weather window for Gemini wind farm at 10 m height
 | Jacking | Operability | 
 |  | Jacking | Lifting
Max wave height (m) | 1.80 | 1.80 | 3.60
Max wind speed at sea level (m/s) | 40 | 15 | Not Applicable
Max wind speed at hub level (m/s) | Not Applicable | Not Applicable | 20
Weather restriction of Van Oord’s Aeolus vessel
= 1.19
7.83 – 9.78 m/s
10 days to repair 1 gearbox
30th of March, 28th of April, and 27th of May 2020 were forecasted to be the weather window with the weakest and safe wind speed in March, April, and May in 2020

## Slide 26
Wind speed trend
Mar
Apr
May
Long-term forecast
Long-term wind speed prediction
Average daily mean wind speed
- Weather window forecast and selection
- Scheduling and sharing the jack-up vessel between wind farms
Short-term prediction with hourly data
- Accessibility & safety of O&M activities on site
- Determine the trade-off between the revenue gained by the delay and demurrage rate
Weather window analysis process
Short-term forecast
30th
28th
27th

## Slide 27
Residual checks of NARX(44,1,23)24 for the 28th March 2020
Residuals check of NAR(44,1,22)24 for the 28th March 2020
Non-linear Autoregressive Neural Network without exogenous input was selected since its residuals were not correlated

## Slide 28
Chart: Real and forecasted wind speed at 10-meter height from 29th to 31th March and 27th to 29th April 2020
Chart: Real and forecasted wind power from 29th to 31st March and 27th to 29th April 2020
NAR(44,1,22)24 and NAR(44,1,40)24 provide reliable hourly mean wind speed and wave height forecast on the 29th, the 30th of March 2020, and the 27th, 28th of April 2020 respectively (MAPE less than 15%)
NAR model could not forecast the hourly mean wind speed of the 31st March and 29th April accurately
NAR model could only forecast the hourly energy output on the 29th and 30th March with acceptable accuracy
Chart: Real and forecasted wave height from 29th to 31st March and 27th to 29th April 2020
Notes: Because the Neural Network is a black-box model, we could not explain its relationship between parameters and lagged input like a normal autoregression model. However, if we compared the forecasted values with the real values of that day and the same days in previous years, we might have some clues. Since the NAR(44,1,22)24 learned from 44-hour lagged data, its 24-step ahead prediction could not deviate too much from the past data. Therefore, it could not capture the sudden large drop in the real observations of the wind speed on these days in 2020 well. This sudden change might be because 2020 was an abnormal year in the Netherlands in which many unpredicted and never-before-seen extreme weather events happened, namely the spring drought and the warmest March in history. Therefore, we can only rely on the prediction of the 29th, 30th of March 2020, and the 27th, 28th of April 2020 for wind speed analysis https://www.amsterdamiww.com/water-solutions-3-risks-and-resilience/more-drought-in-the-netherlands/
https://www.iamexpat.nl/lifestyle/lifestyle-news/tuesday-officially-warmest-march-22-ever-recorded-Netherlands
These large errors might be due to the inconsistency in the energy output data of the Gemini wind farm which was aggregated from The Dutch National offshore wind energy production. We aggregated the nominal wind energy capacity of this wind farm without considering the energy lost due to daily and major maintenance during the period under the study. Therefore, with the hourly mean wind speed of 7.14 m/s at hub height level, each turbine produced 622.87 kWh on average on 27th April 2018, 2133.62 kWh on average on 27th April 2019, and 1910.34 kWh on average 30th March 2020. However, for the same model of a wind turbine, it should produce the same amount of wind energy per given wind speed. Moreover, the real power generated was close to zero in many observations (Figure 38), they also inflated the MAPE exponentially based on the formula (14).

## Slide 29
Chart: Real and forecasted wind speed at 10-meter height from 29th to 31th March and 27th to 29th April 2020
Hourly mean wind speed and energy prediction on the 29th and 30th March were reliable but did not satisfy the safety standards
Chart: Revenue of real and forecasted power per turbine per day from 29th to 30th March and 27th to 28th April 2020
| 29/03/2020 | 30/03/2020 | - | - | - | 27/04/2020 | 28/04/2020 | 29/04/2020
Real Power 2020 | 13033.4348 | 7272.3881 | 2379.218 | 1617.261 | 1124.363
Forecasted power 2020 | 11008.3575 | 8336.6424 | 4039.3648 | 4403.8417 | 4297.3161
28th – 29th April (assume the prediction is accurate)
Predicted gain 107 euros per turbine
Chart: Real and forecasted wave height from 29th to 31st March and 27th to 29th April 2020

## Slide 30
The wind farm operators should not delay the maintenance service for better wind energy generation since the revenue gained could not offset the much higher demurrage rate in the summer
119813 euros per day
Chart: Revenue of real and forecasted power per turbine per day from 29th to 30th March and 27th to 28th April 2020
| 29/03/2020 | 30/03/2020 | - | - | - | 27/04/2020 | 28/04/2020 | 29/04/2020
Real Power 2020 | 13033.4348 | 7272.3881 | 2379.218 | 1617.261 | 1124.363
Forecasted power 2020 | 11008.3575 | 8336.6424 | 4039.3648 | 4403.8417 | 4297.3161
(4404-4297)x150 = 16050 euros
Demurrage rate
Revenue gained from delay in maintenance
Revenue gained from delay in maintenance
Demurrage rate

## Slide 31
Suggestion for offshore wind energy market application
RECOMMENDATION & LIMITATION
Conclusion & further improvements
Questions & Answer

## Slide 32
Suggestion for offshore wind energy market application
WA,WB: Wind farm A, B
HA, HB: Harbor A, B
Wind speed prediction enables jack-up vessel sharing between offshore wind farms
Increase from 52 to 110 mil
45% cost-benefit (6.5 mil Euro)
Vessel utilization 89.5%
5
Weather data analysis enable automation of O&M planning

## Slide 33
Limitation & Further improvements
Long computation time
XGboost imputaiton
Short forecast horizon of NAR
Long Short-term Memory Recurrent Neural Network
Unstable prediction accuracy
Parameter optimization methods
Lack of interpretation
Black box interpretation methods
Externality of research
Apply the analysis process to different sites
Indirect energy output data
Collaborate with wind farm for more authentic data
Notes: The first limitation is the computation time of the machine learning models for missing values imputation and short-term prediction. For the missing value imputation model, we recommend stronger machine learning methods such as Multiple Imputation through XGboost (Deng and Lumley, 2021). This method is the fastest implementation of gradient boosted trees available in R. It can capture the interactions, variability, and non-linear relations while maintaining high computational efficiency. For short-term prediction using a Non-linear Autoregressive Neural Network, we suggested running our models on cloud services to take advantage of its computation power and reduce running time compared to our personal computer.
The second limitation of this work is the forecasting horizon of the Non-linear Autoregressive Neural Network model. Since this method can only make a reliable 24-step ahead forecast for hourly data. It restricts the wind farm operators to organize the maintenance and operation activities on-site only one day ahead of time. We suggest applying the Bayesian Neural Network (Mohsin, Ramli, and Imdad, 2021) or Long Short-Term Memory Recurrent Neural Network (Akram and El, 2016) to predict the wind speed and wind energy 72 hours ahead of time. This longer forecasting horizon will be more beneficial to the orchestra of operation and maintenance service of the offshore wind farm.
The third limitation of the Non-linear Autoregressive Neural Network in this thesis is the unstable prediction accuracy and model interpretability. This method performs very well on some days for wind speed, wind power, and wave height with the MAPE values of less than around 25%, however, its errors can reach approximately 2090% on other days. Therefore, we recommend applying parameter optimization methods to improve the model prediction results such as the novel hybrid forecasting system of ensemble empirical mode decomposition, extreme learning machine, and multi-objective grey wolf optimization(Wu et al., 2020) to balance the accuracy and stability. For the interpretability of the model, we need further research on this topic to improve the model or we can, instead, Fourier ARMA as the last resort if the model interpretation is necessary.
In addition, since the thesis was written to forecast the weather window in 2020, the prediction is only valid in the Gemini location in 2020, we recommend the users to update the most current weather data, wave height, and wind energy at your location to make the long-term and short-term forecasting before planning the O&M activities and chartering the jack-up vessel in the future.
Finally, the large errors in the wind energy prediction may mostly be due to the indirect calculation of Gemini wind farm’s wind energy output which did not consider the energy lost due to daily and major maintenance during the period under the study instead of the actual energy output produced by the wind farm itself. Therefore, the prediction will be more accurate if we can collect the actual energy output which is confidential.

## Slide 34
Conclusion
RQ1
How can the offshore wind farm operator forecast the wind speed over a short-term and long-term period?
RQ2
How can the offshore wind farm operator forecast the wave height over a short-term period?
RQ3
How should the wind farm operator charter the jack-up vessel, in which season of the year, on which day, and for how long given certain maintenance needs?
RQ4
RQ5
How can the wind farm operator determine the trade-off between the revenue gained by 1 day/1 week/1 month delay in maintenance for more energy generation thanks to better weather?
How can the wind farm operator organize the jack-up vessel to conduct maintenance on the wind farm by establishing the trade-off between revenue of the wind farm gained in the delay and the demurrage rate of the jack-up vessel?
F-ARMA(3,2)x(1,0,0)xTemp
NAR(44,1,22)24 & NAR(44,1,40)24
NAR(42,1,22)24
In 2020, from March to May. More specifically, around the 30th of March, 28th of April, and 27th of May 2020 respectively for the jack-up vessel
Predicted gain 2671.71 euros per turbine if delay 29th – 30th March 2022
The wind farm operator should not delay the maintenance schedule for better weather condition
Predicted gain 107 euros per turbine if delay 28th – 29th March 2022

## Slide 35
THANK YOU

## Slide 36: ABOUT ME
“Be the change that you wish to see in the world” – Mahatma Gandhi
Bachelor in International Business & Economics
Natural Resources Management and Environmental Issues
Master in Data Science & Marketing Analytics
Physical Distribution Process Engineer Intern
Case Team Assistant – Temporary Contract
Quantitative Data Analyst Trainee – Client Service Department
Data Analysis
Project Management & Coordination
Fund-raising
Persistent & Creativity
Dare to try & Dare to fail

## Slide 37
THESIS CONTRIBUTION
DATA SOURCES
Supplements (Schouten, 2019) research by predicting the difference in energy output and downtime cost for certain delay
Provides Synthetic Climate Data Prediction of both the wind speed and the wave height for the accessibility and operative analysis
Provides long-term planning for jack-up vessel
Provides short-term accessibility assessment for jack-up vessel
Applies most updated data
EXCEPT FOR THE FAILURE ANALYSIS, THE THESIS COVERS ALMOST ALL THE TOPICS OF OFFSHORE WIND FARM OPERATION & MAINTENANCE RESEARCH
CMEMS
Van Oord Aeolus sea keeping specification (Crol, 2015)
Jack-up vessel charter rate (Dalgic, Lazakis, Turan, et al., 2015)
2011 - 2020
2018 - 2021
2017 - 2020
2015
2015
Hourly level
Hourly level
Every 15 minutes
m and m/s
Pound Sterling
2002

## Slide 38
Data statistics
Variable name | Unit | Mean | Max | Min
YYYYMMDD | - | - | - | -
HH (Time) | - | - | - | -
Mean_wind_speed | m/s | 6.99 | 25 | 0
Temperature | degrees Celsius | 10.76 | 34.1 | -9.10
Variable name | Unit | Mean | Max | Min
Index | Year – Month – Day | - | - | -
Mean_wind_speed | m/s | 6.94 | 17.92 | 1.29
Temperature | degrees Celsius | 11.05 | 26.53 | -5.79
Variable name | Definition | Min | Max | Mean
Time | Date (YYYY=year, MM=month, DD=day) and Time (HH=hour, MM=minute, SS=second) | - | - | -
VHM0 | Significant wave height (m) | 0.15 | 6.35 | 1.40
 | Jacking | Operability | 
 |  | Jacking | Lifting
Max wave height (m) | 1.80 | 1.80 | 3.60
Max wind speed at sea level (m/s) | 40 | 15 | Not Applicable
Max wind speed at hub level (m/s) | Not Applicable | Not Applicable | 20
Index | Wind electricity generation (kWh)
Min | 0
Mean | 1677.80
Max | 3814.4
Parameter | Value
Daily charter rate (Pound) | 172500 Pound/day (April – September)
 | 116250 Pound/day (October – March)
Demurrage (Pound) | +30% daily rate
Jack-up/down period | 3 hours
Hub removal time | 8 hours
Excluding missing values, there were certain hours without any wind
However, there was no day without wind from 2014-2019
After conversion and transformation, the wind energy statistics make sense since the maximum nominal energy generated by SIEMEN SWT 4.0 – 130 turbine is 4000 kwh
Table 4: Variable definition and description of wave height data set 2018-2021
Table 6: Weather restriction of Van Oord’s Aeolus vessel
Jack-up vessel charter rate is seasonal which is lower in the winter and higher in the summer
17 cent/kwh
7.83 – 9.78 m/s
3 – 4 m
Table 1: Hourly weather data set descriptions excluding missing values 2018-2021
Table 2: Average daily mean wind speed 2014-2019
Table 3: Hourly weather data set descriptions excluding missing values 2018-2021

## Slide 39
Chart: Hourly mean wind speed 2011-2012 after imputation with mtry = √10 and ntree=10
Chart: Hourly mean wind speed 2011-2012 after imputatoin with mtry = √10 and ntree=25
 |  | ntree = 2 and mtry = | ntree = 10 and mtry = | ntree = 25 and mtry = | ntree = 50 and mtry = 7
OOB error (MSE) | Wind_direction | 4401.25 | 2695.07 | 2900.00 | 2561.43
 | Mean_wind_speed | 0.79 | 0.58 | 0.52 | 0.52
 | Max_wind_gust | 1.33 | 0.96 | 0.87 | 0.83
 | Temperature | 1.49 | 1.10 | 0.88 | 0.49
 | Air_pressure | 0.36 | 0.22 | 0.18 | 0.13
 | Relative_humidity | 44.52 | 31.66 | 23.94 | 20.43
Computation time (minutes) |  | 11.23 | 44 | 154.87 | 352.51
 |  |  |  |  | ntree = 50 and mtry = 7
OOB error (MSE) | Wind_direction | 4401.25 | 2695.07 | 2900.00 | 2561.43
 | Mean_wind_speed | 0.79 | 0.58 | 0.52 | 0.52
 | Max_wind_gust | 1.33 | 0.96 | 0.87 | 0.83
 | Temperature | 1.49 | 1.10 | 0.88 | 0.49
 | Air_pressure | 0.36 | 0.22 | 0.18 | 0.13
 | Relative_humidity | 44.52 | 31.66 | 23.94 | 20.43
Computation time (minutes) |  | 11.23 | 44 | 154.87 | 352.51

## Slide 40
Wind speed trend
Jan
Feb
Mar
Apr
May
Wind speed trend
Mar
Apr
May
Long-term forecast
Short-term forecast
Long-term wind speed prediction
Average daily mean wind speed
- Weather window forecast and selection
- Scheduling and sharing the jack-up vessel between wind farms
Weather window of 1 day before and after
30th March